## Slide 1: Programming TYT Handhelds
MD-380/390 and MD-UV380/390
Updated 2021/01/01
Presented by KF7HVM - Masen
https://www.kf7hvm.com/info/tyt/

## Slide 2: Models and Limits
MD-380 / 390
Monoband, either UHF or VHF
1000 Channels
10,000 Contacts
250 Scan lists (of 32 channels each)
250 Zones (of 16 channels each)
Has custom firmware
MD-UV380 / 390
Dual band + commercial
3000 Channels
10,000 / 120K Contacts
250 Scan lists (of 64 channels each)
250 Zones (of 64 channels each)
390 variants include GPS*

## Slide 3: Stock Software
Similar to other Chinese manufacturers
Very limited functionality for managing large, complex code plugs
  Cannot reorder zones
  Cannot import/export zones, scanlists, grouplists
  Requires licensed Microsoft Excel for full import/export function
Windows-only; Different version per model
Annoyances and bugs – tab index, no indication of invalid data

## Slide 4: Third Party Software: EditCP
Drag / Drop; Copy between codeplugs
Support multiple radio models
JSON import/export
Data validation
Upload Codeplug, Firmwares and contact list
Windows or Linux
Identical field names and placement, easy for those familiar with stock CPS
https://www.farnsworth.org/dale/codeplug/editcp/

## Slide 5: Third Party Software: N0GSG Contact Manager
Supports multiple radio types, including Anytone
Structural import/export allows for sharing across radio types
Channel Mass Change
Zone Wizard
Download, filter, and export DMR ID Database
Windows only, but runs in Wine
http://n0gsg.com/contact-manager/

## Slide 6: General Settings
Radio Name: callsign
Radio ID: DMR ID
Scan Digital / Analog Hang Time
Talk Permit Tone
Enable Contacts CSV: UV380/390 with ContactCSV firmware only!

## Slide 7: Manual Programming
“Give a man a codeplug and he operates for a day;
Teach a man to Codeplug and He Operates for a Lifetime”

## Slide 8: DMR Objects
“Contact”, “Digital Contact”, “Talkgroup”
  Correlate a DMR ID to a name
“Group List”, “RX List”, “TG List”
  A list of contacts that will be heard on a channel
“Channel”
  Frequency, offset, color code, TX Contact, RX List
“Scan List”
  A list of up to 32 (64 for UV) channels to scan as a group
“Zone”
  A list of up to 16 channels (MD-380)
  2 lists of up to 64 channels (MD-UV380)

## Slide 9: Contacts
Private calls are not typically used in Amateur deployments, except to map Callsigns to DMR ID*

## Slide 10: Digital Simplex
Hotspot or P2P simplex
Favor TS 1, TG 99
Admit Criteria: Always
Tx Offset: 0

## Slide 11: Group List
Allows a single channel to monitor multiple talkgroups
Helps avoid “stealing” the timeslot away from an ongoing QSO
Place all TS 1 talkgroups into a list and all TS 2 talkgroups into another list.
  Each channel with a TX Contact on a given timeslot should include the corresponding group list.

## Slide 12: Digital Repeater
1 Channel per TX Talkgroup!
Admit Criteria: Color Code
Contact Name: Washington 1
RX Group List: PNWDigital TS 1
Color Code: 1
Repeater Slot: 1
In Call Criteria:
  Follow Admit Criteria

## Slide 13: Analog Simplex
Simple
Bandwidth: 25
Admit Criteria: Always

## Slide 14: Analog Repeater
Tx Offset: +5
Admit Criteria: CTCSS/DCS
CTCSS/DCS Decode, Encode
Leave signaling options OFF!

## Slide 15: Zones
Channels MUST be in a zone to be accessible on the radio
MD-380 Zones are 16 channels
MD-UV380 Zones are 2x 64 channels

## Slide 16: ScanList
Channels to scan as a group
Required for scan functionality. Zones cannot be scanned as-is.
Priority Channel: These channels will be checked 50% of the time
Tx Designated: Which channel transmits during a scan
Priority Sample Time: How often to check the priority channels while receiving another signal.
Hold Times are global: see General Settings

## Slide 17: Starting from Existing Codeplug
EditCp allows multiple codeplugs to be open at the same time
Drag / Drop or Copy / Paste between open codeplugs
  Automatically copies dependent objects
N0GSG Contact Manager allows direct import of contacts and channels from existing codeplugs

## Slide 18: Contacts Database
MD-380: only really supported with 380toolz custom firmware
MD-UV380: Firmware versions beginning with “V” support “ContactsCSV” (up to 120K entries)
With 160K+ IDs and growing, trimming the list is necessary
  RadioID.net has a custom db generator (9.99/yr): https://contacts.radioid.net/generator
  N0GSG Contact Manager can download and filter the list for free!

## Slide 19: N0GsG Contact Manager
Search by country, name, call, etc
Format the records as desired
Use EditCp to upload the database to MD380 or MD-UV380

## Slide 20: Codeplug Generators
K7ABD - https://www.k7abd.net/anytone-config-builder/
cps-import-builder - https://github.com/n7ekb/cps-import-builder
dzcb - https://github.com/masenf/dzcb